## Slide 1: Low Dropout Voltage Regulator
ECE531 Mixed-Signal VLSI Design

## Slide 2: Types of Voltage Regulator
Zener diode voltage regulation
  Simple, low cost
Switching regulator
  High efficiency, but noisy and bulky
    Buck DC-DC converter
    Boost converter
    Inverting converter
    Flyback converter
Linear regulator
  Less noisy, relatively simply circuit structure, wide bandwidth, but less efficient
    Low Dropout regulator

## Slide 3: Boost converter
Basic circuit structure
When Vout<Vin, diode conducts to charge Vout to Vin level. Hence, the following discussion assume Vout>Vin
When switch is close (on),
  the diode is reverse biased and hence off
  The voltage across the inductor is Vin and the rate of the change of the inductor current
Maxim Application note AN2031 DC_DC converter Tutorial
Maxim Application note AN2031 DC_DC converter Tutorial

## Slide 4: Boost converter
When the switch is open (off)
  The inductor current continuously flows, forcing the diode forward biasing and charging output capacitor. The inductor voltage is:
    Where is the diode voltage when it is forward basing
  The inductor current gradually decreases with the slope of
Switch close
Switch open
Charging cycle duration ton
Discharging cycle duration toff ton

## Slide 5: Boost converter
When the circuit reaches steady state, the inductor current at the beginning of the charging cycle is the same as that at the end of the discharging cycle.
Define the switching cycle
Switch close
Switch open
Charging cycle duration ton
Discharging cycle duration toff ton

## Slide 6: Boost converter
We can solve Vout as
Since D<1, Vout>Vin.
Vout value can be varied by changing switch duty cycle, which is controlled a clock signal
The regulator output will contain large noise energy at the clock frequency. Filters can be used to attenuate it.
The above analysis relies on many simplifications, such as
  It assumes the voltage at the right side terminal of the inductor jumps from 0 to Vout+VDon immediately after opening the switch

## Slide 7: Boost converter
clk
Vout
V(n1)
1.2V
2.4V
Iindctor
After opening switch, inductor current continues to increases because Vn1<Vin
In this case, is larger than the clock pulse width
The waveform shows and hence

## Slide 8: Boost Converter
clk
Vout
V(n1)
Constant Inductor voltage
Constant Inductor voltage
Example

## Slide 9: Buck Converter
Vout will be smaller than Vin
When switch is close, diode is reverse biasing and inductor current charges capacitor:
When switch is open, the inductor current continues to flow, forcing the diode forward biasing and
  Assume diode VDon=0
Similarly,
Thus,

## Slide 10: Inverting Converter
It generates negative voltage
When switch is close, diode is reverse biasing, and
When switch is open, inductor current continues to flow, forcing diode forward biasing and discharging output capacitor.
Similarly, we have and hence
  When ,
  When ,

## Slide 11: Flyback Converter
It uses transformer to isolate Vin and Vout
When the switch is close, current flows the primary winding. The diode is reverse biasing to block current flowing in the secondary winding
When the switch is open, the current of the secondary winding forward biases the diode and charge output capacitor
Assume the following transformer parameters
  Primary winding: inductance L1, number of windings or turns N1
  Secondary winding: inductance L2, number of windings N2
Magnetic flux or

## Slide 12: Flyback Converter
At steady state, the magnetic flux built be the primary winding current I1 equals the flux dissipated by driving the secondary winding current I2.
  When the switch is close during , I1 increases at the rate of
  When the switch if off during , I2 decreases at the rate of
  Thus,
This leads to
  Assume N1=N2
    When , ; When ,
    It is also called buck-boost converter

## Slide 13: Control signals for switching converters
Pulse width modulation technique is typically used to control the duty cycle of the switches
Maxim Application note AN2031 DC_DC converter Tutorial
comparator
Error Amplifier

## Slide 14: Control signals for switching converters
Expected output
If , increase, D increases. Since for boost converter, this causes increases.

## Slide 15: Control signals for switching converters
Simulation
1.598V
1.631V

## Slide 16: Capacitor-only voltage down converter
Clk1 and clk2 are non overlapping clock with period T
The load drains a constant current Iload
When clk1=1, C1 is charged to Vin
When clk2=1, charge redistribution between C1 and C2. Assume this process is fast and hence the clk2 pulse is narrow
  Output voltage changes to after charge redistribution
  Ignore the effect of Iload, the charge is moved from C1 to C2 is:

## Slide 17: Capacitor-only voltage down converter
Between two clk2 pulses, the output voltage decreases by . Since clk2 pulse is narrow, this duration is approximately T. Thus:
The clock period can be selected according to
Or for a given clock period

## Slide 18: Capacitor-only voltage up converter
In clk1 phase, both capacitors are charged to Vin
In clk2 phase, the initial voltage of the two stacked capacitors is 2Vin, and then changes to due to charge redistribution
  The total charge transferred to C2 is:
Similarly, we have

## Slide 19: Capacitor-only voltage up converter
We have:
If , we have
Circuit implementation

## Slide 20: Capacitor-only negative voltage converter
In clk1 phase, C1 is charged to Vin
In clk2 phase, the potential at the bottom plate of C1 is initially –Vin. After the charge redistribution, it becomes .
The charge moved from C1 to C2 is:

## Slide 21: Capacitor-only negative voltage converter
Also, we have
Thus
  If , Vout is negative
Circuit implementation

## Slide 22: Low dropout regulator (LDO)
LDO behaviors like a voltage divider.
  The load impedance is the bottom resistor
  The series pass element is the top resistor, whose impedance is controlled by the control circuit
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072

## Slide 23: Low dropout regulator (LDO)
Pro
  LDO output is less noisy compared to switching regulator
  It has high power ripple rejection ratio
  Simple circuit structure
Cons
  Pass element consumes energy. Hence low efficiency and potential thermal management issue
  The voltage drop along the pass element is preferred to be small (However, too small will fail the LDO operation)

## Slide 24: Low dropout regulator (LDO)
Assume the pass element is an NMOS transistor (Though PMOS is more widely used)
The transistor may operate in linear region but often is required to operate in saturation region. Their equivalent circuits are:
Note that
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072

## Slide 25: Low dropout regulator (LDO)
When the NMOS is in saturation, it functions as voltage controlled current source and the LDO regulates the output
When becomes small, the NMOS is in linear region. It functions as a resistor and LDO will not be able to regulate the output
The voltage at which the LDO fails to regulate output is called dropout voltage.

## Slide 26: LDO Topology
Pass element can be bipolar or MOS transistors. In CMOS circuit, PMOS is often used
Vref can be provided by Bandgap or externally
The voltage divider enables Vref<Vout
R1
R2
VS

## Slide 27: LDO ground current
Quiescent current, or ground current, is the difference between input and output currents.
  Ground current is caused by the voltage reference, error amplifier, etc.
Efficiency:

## Slide 28: LDO performance metrics
Load regulation is a measure of the circuit’s ability to maintain the specified output voltage under varying load conditions.
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072

## Slide 29: Load Regulation
gm is the trans-conductance of the power device
A is the gain of the error amplifier
Assume there is a load current change and the voltage change is
  increasing error amplifier gain A and power transistor transconductance improves load regulation
A

## Slide 30: Line regulation
Line regulation is a measure of the circuit’s ability to maintain the specified output voltage with varying input voltage
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072

## Slide 31: Line regulation
A

## Slide 32: LDO transient response
Transient response refers to how LDO output voltage settle after a step change of output current or input voltage
If no capacitor is present at the LDO output, a load current change can dramatically drive the output voltage away from its desirable value before the control loop take effects
  The response time of the control loop is related to the bandwidth of the control loop

## Slide 33: LDO transient response
A large capacitor can be added at the LDO output node which serves as a charge tank to stabilize the output voltage before the control loop to take effect
This results in two poles in the system frequency response: one is the output node pole Po and the second is the opamp dominant pole Pa
This typically leads to an unstable system

## Slide 34: LDO transient response
To make system stable, a zero can be created by adding a resistor in series with the output capacitor
However, the ESR also causes voltage drop when a large current is drained from the output capacitor. To address this, a bypass capacitor can be added

## Slide 35: Frequency response
Error amplifier contribute a pole
Impedance of output node
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072
Reference

## Slide 36: Frequency response
CO>>Cb
S. Lee, Technical Review of Low Dropout Voltage Regulator Operation and Performance, TI Application Note, SLVA072
Reference

## Slide 37: Frequency response
Pole and zero placement to keep LDO stable
Pole Pb smaller than unit gain frequency (large ESR) leading to unstable system
Zero is higher than unit gain frequency (small ESR) leading to unstable system

## Slide 38: Improving LDO transient responses with double control loop
Two control loops can be used to improve LDO transient responses
  One is slow loop with high gain amplifier for accuracy
  The other one is fast loop that has simple structure to improve transient response
Kosta Luria, Joseph Shor, Michael Zelikson, Alex Lyakhov, Dual-Use Low-Drop-Out Regulator / Power Gate with Linear and On-Off Conduction Modes for Microprocessor On-Die Supply Voltages in 14nm, 2015 IEEE International Solid-State Circuits Conference
Reference

## Slide 39: Double Loop LDO
Slow loop
  VCCGVSETVn1 (M2 is a CS amplifier) Vn3 (M5 is a CG amplifier)IDS1 VCCG
  VCCG follows the relation
Reference

## Slide 40: Double Loop LDO
Fast loop
  VCCGVn1 (M2 is a CG amplifier) Vn3 (M5 is a CG amplifier)IDS1 VCCG
  It can show that the output resistance of the fast loop circuit alone (supper source follower, or flipped source follower) has small output resistance. Output current change does not cause large voltage variation.
Reference

## Slide 41: Double Loop LDO
Peter Hazucha, Tanay Karnik, Area-Efficient Linear Regulator With Ultra-Fast Load Regulation, IEEE JOURNAL OF SOLID-STATE CIRCUITS, VOL. 40, NO. 4, APRIL 2005
Reference

## Slide 42: Double Loop LDO
Output impedance estimation
A
Reference

## Slide 43: Frequency compensation
Along the slow loop, nodes 1, 2, 3, 4 introduce poles
Nodes 2 and 4 have low resistance. Thus, their poles are at high frequency
Nodes 1 and 3 has high resistance, their poles are at low frequency
To make one pole the dominant pole, Rc and Cc are added
Cut the loop open here and perform AC analysis to find frequency response of the open loop gain
1
2
3
4
Reference

## Slide 44: Frequency compensation
Capacitor multiplier
Vout
Iout
Reference

## Slide 45: Frequency compensation
It introduces a pole and zero
Reference

## Slide 46: Digital LDO circuits
With low supply voltage, it is difficult to design power efficient high-gain wide bandwidth amplifier that required in analog LDO circuits
Digital LDO circuits
  Error amplifier is replaced by a comparator
  The single pass element (PMOS device) is replaced by an array of small pass devices
Yasuyuki Okuma, Koichi Ishida, et al. 0.5-V Input Digital LDO with 98.7% Current Efficiency and 2.7-μA Quiescent Current in 65nm CMOS

## Slide 47: Digital LDO circuits
The controller controls how many PMOS transistors are conducting
When Vout<Vref, (comparator output is 0), more transistors need to be conducting
When Vout>Vref (comparator output is 1), less transistors need to be conducting
A specially designed shift register can be used as the control circuit.

## Slide 48: Digital LDO circuit
Shift register implementation
Digital LDO output

## Slide 49: Digital LDO circuit
In the previous design, only one transistor can be turned on or off during one clock cycle. Also, the update rate is controlled by the clock frequency
Such limitations lead to slow transient responses. Various techniques are developed to improve transient responses
  Shift multiple bits if there is large voltage variation
  Asynchronous shifting operation that leads to fast update when there is a large voltage variation

## Slide 50: Digital LDO circuits
Low voltage MOS devices can be used as the pass devices to reduce area and improve transient response (less number of power transistors).
  In conventional digital design, the gate of conducting PMOS device is tied to ground and hence |VGS|=Vin.
  Low voltage PMOS require smaller |VGS| and hence the gate of conducting PMOS has to be tied to a level VS
Masafumi Onouchi, Kazuo Otsuga, et al. A 1.39-V Input Fast-Transient-Response Digital LDO Composed of Low-Voltage MOS Transistors in 40-nm CMOS Process

## Slide 51: Digital LDO circuit
VSSV generation circuit
Other potential advantage of not tying power device to ground when it is conducting
Vin
Vout
0
Transistor in linear region small ro
Vin
Vout
Vssv
Transistor may be saturation region large ro

## Slide 52: Other digital LDO
Instead of using comparator to detect voltage difference, other techniques can be used to monitor the output voltage
  Voltage controlled delay line or voltage controlled oscillator
  Circuit performance monitoring
Koji Hirairi, et. al. 13% Power Reduction in 16b Integer Unit in 40nm CMOS by Adaptive Power Supply Voltage Control with Parity-Based Error Prediction and Detection (PEPD) and Fully Integrated Digital LDO

## Slide 53: Model of digital LDO
Digital LDO consists of both discrete-time and continuous time systems
Comparator is one-bit ADC
Digital gain can be adjusted by changing how many bit is shifted within one clock cycle
Saad Bin Nasir, Youngtak Lee, Arijit Raychowdhury, Modeling and Analysis of System Stability in a Distributed Power Delivery Network with Embedded Digital Linear Regulators
Reference

## Slide 54: Model of digital LDO
Open loop transfer function
  KD digital gain; T clock period; KA analog gain; pole at output node
S-domain to Z-domain
  Let
G
G
Reference

## Slide 55: Stability of digital LDO
Closed loop transfer function
Reference